## Slide 1: GNN2: Dataset Generation & Initial Training
IEEE 34-Bus Power Flow Surrogate

## Slide 2: GNN2 Notebook Overview
Colab setup: clone repo, install torch, torch-geometric, opendssdirect
Dataset generation: 5 datasets from OpenDSS power-flow solves
Graph sanity checks: bidirectionality, edges, node features
Initial GNN training: Original, Injection, Load-type datasets
Unified config exploration: light, medium, heavy, deep per dataset

## Slide 3: Dataset Generation Pipeline (Step by Step)
1. Read OpenDSS model, set daily mode (5-min, 288 pts/day)
2. Find load/irradiance profile CSVs from DSS
3. Build bus-phase node list (95 nodes)
4. Extract static phase edges (R, X, C) → 184 edges
5. Sample scenarios: P_load, Q_load, P_PV from BASELINE × RANGES
6. Select timestamps: 3 profiles (load, PV, net) with anchors + equal-pop bins
7. Apply snapshot: device setpoints + noise, solve OpenDSS
8. Store node features and voltage targets

## Slide 4
Five Datasets
# | Name | Output | Features | Target
1 | Original | gnn_samples_out | p_load, q_load, p_pv (3) | vmag_pu
2 | Injection | gnn_samples_inj_full | p_inj, q_inj (2) | vmag_pu
3 | Load-type | gnn_samples_loadtype_full | 13 (M1/M2/M4/M5, dist, balance) | vmag_pu
4 | Delta-V | gnn_samples_deltav_full | 14 (+ vmag_zero) | vmag_delta_pu
5 | Delta-V 5× | gnn_samples_deltav_5x_full | 14 (same) | vmag_delta_pu

## Slide 5: Output Files (per dataset)
gnn_edges_phase_static.csv — edges with R_full, X_full, C_full
gnn_node_index_master.csv — node names and indices
gnn_sample_meta.csv — sample_id, scenario_id, P_load, Q_load, P_pv, m_load, m_pv
gnn_node_features_and_targets.csv — features + vmag_pu (or vmag_delta_pu)

## Slide 6: Time Selection: 3 Profiles + Anchors
Three profiles: load (mL), PV (mPV), net (P_load×mL − P_pv×mPV)
Split K snapshots across profiles (~1/3 each)
Anchors: min and max time index per profile (extreme operating points)
Equal-population bins: rank-based, same count per bin
Ensures coverage of load-high, PV-high, net-stress regions

## Slide 7: Graph Sanity Check
Bidirectionality: every edge (a→b) has reverse (b→a)
Transformer/regulator edges: 832↔888, 814↔814r, 852↔852r
One-sample node features: verify feature columns
Nominal power balance: sum_load − sum_pv ≈ p_sys_balance
Delta-V summary: vmag_zero_pv_pu, vmag_delta_pu (dataset 4)

## Slide 8: GNN Architecture (PFIdentityGNN)
Message-passing GNN on phase-level graph
Node embeddings: learnable per-node (identity)
Edge features: R_full, X_full from OpenDSS
Message: MLP(h_j + edge_attr + edge_emb)
Readout: MLP → per-node voltage (vmag_pu or vmag_delta_pu)

## Slide 9: Nominal vs Realized Power Comparison
Runs OpenDSS for 10 samples; compares nominal (set) vs realized (power-flow) values
Loads: per-load and per-node; PV: nominal vs realized; Capacitors; Grid (TotalPower)
Sum check: verifies realized P/Q sums ≈ 0 (power balance)
Fix: %Cutin=0 on PV systems (default 2% cut-in caused zero output at low irradiance)

## Slide 10
Initial Training (per dataset)
Dataset | Features | Checkpoint
Original | 3 (p_load, q_load, p_pv) | pf_identity_gnn_best.pt
Injection | 2 (p_inj, q_inj) | pf_identity_gnn_inj_best.pt
Load-type | 13 (load types, dist, balance) | pf_identity_gnn_loadtype_best.pt

## Slide 11: VMAG-only Training & Embedding Inspection
VMAG-only training: outputs vmag_pu only (angle removed); smaller, faster model
Embedding inspection: print node/edge identity embeddings (z_i, r_e) for PFIdentityGNN
Verifies learned per-node and per-edge representations

## Slide 12: Unified Config Exploration
4 configs: light, medium, heavy, deep (varying h_dim, num_layers)
Run each on all 3 datasets (Original, Injection, Load-type)
12 runs total — find best dataset × architecture combination
Load-type typically wins; feeds into GNN3 exploration

## Slide 13: GNN2 Summary
5 datasets generated from OpenDSS with 24h profiles
Nominal vs realized comparison; %Cutin=0 fix for PV
Graph sanity checks ensure valid phase-level topology
PFIdentityGNN trained on Original, Injection, Load-type
Unified config exploration (light, medium, heavy, deep) → feeds GNN3

## Slide 14: Thank You
Questions?