## Slide 1: GNN-Based Power Flow Surrogate
IEEE 34-Bus Distribution Feeder

## Slide 2: Problem & Motivation
Need fast voltage prediction for real-time grid applications
OpenDSS power-flow solves are iterative and slow
Goal: Replace with a GNN surrogate for instant inference

## Slide 3: Approach
Message-passing GNN on phase-level graph (95 nodes, 184 edges)
OpenDSS for ground-truth simulation and dataset generation
PyTorch Geometric for GNN training
5-min resolution (288 timesteps per day)

## Slide 4
Datasets (5 Types)
# | Name | Features | Target | Samples
1 | Original | p_load, q_load, p_pv (3) | vmag_pu | ~192k
2 | Injection | p_inj, q_inj (2) | vmag_pu | ~192k
3 | Load-type | 13 (M1/M2/M4/M5, dist, balance) | vmag_pu | ~192k
4 | Delta-V | 14 (Load-type + vmag_zero) | vmag_delta_pu | 57,600
5 | Delta-V 5× | 14 (same) | vmag_delta_pu | 57,600

## Slide 5: Dataset Generation
Scenario sampling: P_load, Q_load, P_PV from BASELINE × RANGES
24h profiles: load shape mL[t], irradiance mPV[t] from CSV
Time sampling: select_times_three_profiles (load, PV, net bins)
Delta-V fix: Use mL[t], mPV[t] in training to match test-time structure

## Slide 6: GNN Architecture (PFIdentityGNN)
Node embeddings: learnable per-node (identity)
Edge features: R, X from OpenDSS
Message passing: EdgeIdentityMP (MLP on h_j + edge_attr + edge_emb)
Readout: MLP → per-node voltage prediction
Hyperparameters: node_emb, edge_emb, h_dim, num_layers, phase_onehot

## Slide 7
Architecture Exploration (7 Blocks)
Block | Configs | Datasets | Best
1 | 20 nominees | Original, Injection, Load-type | light_xwide
2 | 60 nominees | Same 3 | —
3 | 10 promising | Same 3 | —
4 | 10 to beat Block 3 | Same 3 | —
5 | 8 from Block 4 | Same 3 | light_emb_h96_phase_onehot_depth3_h112
6 | 9 best Load-type | Delta-V | light_xwide_emb_phase_onehot
7 | 9 best | Delta-V 5× | light_xwide_emb_phase_onehot

## Slide 8
Final 7 Models (Best per Dataset)
Block | Dataset | Architecture | Target
1 | Original | medium (h=32, 4L) | vmag_pu
2 | Injection | deep (h=64, 4L) | vmag_pu
3 | Load-type | light_emb_h96 (h=96, 2L) | vmag_pu
4 | Load-type | light_emb_h96_phase_onehot_depth3 | vmag_pu
5 | Load-type | light_emb_h96_phase_onehot_depth3_h112 | vmag_pu
6 | Delta-V | light_xwide_emb_phase_onehot | vmag_delta_pu
7 | Delta-V 5× | light_xwide_emb_phase_onehot | vmag_delta_pu

## Slide 9: Results
Best full voltage (V): Block 5 — MAE ≈ 0.006 pu
Best delta-V: Block 6/7 — MAE ≈ 0.003–0.005 pu
24h overlay plots: OpenDSS vs GNN at observed node
PV sensitivity: 0.7×, 1.0×, 1.3× penetration

## Slide 10: Delta-V Retrain & Voltage Profile Plotting
run_gnn3_deltav_only_train: retrain blocks 6 & 7 on new 24h-profile datasets
plot_voltage_profile_by_operation_point: multi-node, multi-operation-point 24h plots
Explores oscillation-free operation points (P_BASE, Q_BASE, PV_BASE)

## Slide 11: Error Analysis: Spatial and Temporal Breakdown
Spatial: Per-bus error to identify high-error locations
Temporal: Per-timestep error to locate spikes
Used to understand where the model fails

## Slide 12: Key Details
Exploration: 30% data; final training: 100% data
Phase onehot: added in Blocks 4–7 for phase-aware prediction
Batched GNN inference: 288 timesteps in one forward pass
Timing: OpenDSS profile vs full GNN pipeline (zero-PV + build_x + forward)

## Slide 13: Summary
5 datasets: Original, Injection, Load-type, Delta-V, Delta-V 5×
7 exploration blocks, 100+ architecture configs
7 best models, one per dataset type
Delta-V train–test alignment fix (24h profile)
PV sensitivity, error analysis, voltage profile plotting

## Slide 14: Thank You
Questions?